FreeEMS Serial Protocol – IFreeEMS Vanilla

Version 0.0.0 - 23rd December 2010. (Working Draft)
GNU General Public License V3 or later.

Foreword

This document is based on and assumes knowledge of the FreeEMS Serial Protocol – Core document.

The purpose of this document is to define the application functionality and payload data formats for communicating with FreeEMS Vanilla. Not all devices will support all functions, either because they have limited functionality (a display device for example), or because the software versions may differ. Where logging/debug facilities are available, the payload type of unrecognised packets should be noted before discarding them.
Payload Type Definitions

Title: updateBlockInRAM
Description: Replaces a block of RAM memory with the provided data. Some blocks are only allowed to be changed as a whole and not partially, IE, size must match the size of the locationID provided and offset must be zero. General configuration blocks can be adjusted using arbitrary offset and size parameters provided that offset is less than size and size is greater than 0 and less than the locationID size. The locationID provided must have non-zero RAM fields.
Payload ID: 0x0100/256
Length: 7+
Contents: locationID (2), offset (2), size (2), data (1+)

Title: updateBlockInFlash
Description: Exactly the same as updateBlockInRAM except for flash memory, and updates the corresponding RAM region if there is one. The locationID provided must have non-zero flash fields.
Payload ID: 0x0102/258
Length: 7+
Contents: locationID (2), offset (2), size (2), data (1+)

Title: retrieveBlockFromRAM
Description: Exactly as per the title. The locationID provided must have non-zero RAM fields.
Payload ID: 0x0104/260
Length: 2
Contents: locationID (2)
Reply: requestedData (1+)

Title: retrieveBlockFromFlash
Description: Exactly as per the title. The locationID provided must have non-zero flash fields.
Payload ID: 0x0106/262
Length: 2
Contents: locationID (2)
Reply: requestedData (1+)

Title: burnBlockFromRamToFlash
Description: Burn data from live tuned RAM down to persistent flash storage. The locationID provided must have non-zero values for all RAM and flash fields.
Payload ID: 0x0108/264
Length: 2
Contents: locationID (2)

Title: adjustMainTableCell
Description: Adjust a single cell of a main table. The locationID must be that of a main table. The indices must be in range.
Payload ID: 0x012C/300
Length: 8
Contents: locationID (2), RPMIndex (2), LoadIndex (2), CellValue (2)

Title: adjustMainTableRPMAxis
Description: Adjust an RPM axis value of a main table. The locationID must be that of a main table. The index must be less than the length of the axis. The provided RPM value must be between the values of its upper and lower neighbours.
Payload ID: 0x012E/302
Length: 6
Contents: locationID (2), RPMIndex (2), RPMValue (2)

Title: adjustMainTableLoadAxis
Description: Adjust a load axis value of a main table. The locationID must be that of a main table. The index must be less than the length of the axis. The provided load value must be between the values of its upper and lower neighbours.
Payload ID: 0x0130/304
Length: 6
Contents: locationID (2), LoadIndex (2), LoadValue (2)
Title: adjust2dTableAxis
Description: The index must be less than the length of the axis. The provided axis value must be between the values of its upper and lower neighbours.
Payload ID: 0x0132/306
Length: 6
Contents: locationID (2), AxisIndex (2), AxisValue (2)

Title: adjust2dTableCell
Description:The index must be less than the number of cells.
Payload ID: 0x0134/308
Length: 6
Contents: locationID (2), CellIndex (2), CellValue (2)

Title: requestBasicDatalog
Description: Request a basic datalog packet to be sent back, useful when not streaming. The optional payload contents are the truncation length to be used. If it is not provided the configured truncation length will be used just as in asynchronous mode.
Payload ID: 0x0190/400
Length: 0 or 2
Contents: Optional Length (2)
Reply: requestedData (1+)

Title: requestConfigurableDatalog
Description: UNIMPLEMENTED
Payload ID: 0x0192/402
Length: ?
Contents: ?
Reply: requestedData (1+)

Title: setAsyncDatalogType
Description: Configure the asynchronous datalog type 0x00/0 is off, other values turn specific types of logging on.
Payload ID: 0x0194/404
Length: 1
Contents: datalogType (1)

Title: forwardPacketOverCAN
Description: UNIMPLEMENTED
Payload ID: 0x01F4/500
Length: ?
Contents: ?

Title: forwardPacketOverOtherUART
Description: UNIMPLEMENTED
Payload ID: 0x01F6/502
Length: ?
Contents: ?

Title: retrieveArbitraryMemory
Description: As per the title, for debugging ONLY, could be removed in future.
Payload ID: 0x0258/600
Length: 6
Contents: length (2), address (2), RAMPage (1), FlashPage (1)
Reply: Original contents (6), requestedData (length)