FreeEMS Serial Protocol – IFreeEMS Vanilla

Version 0.0.0 - 11th January 2011. (Working Draft)
GNU General Public License V3 or later.

Foreword

This document is based on and assumes knowledge of the FreeEMS Serial Protocol – Core document.

The purpose of this document is to define the application functionality and payload data formats for communicating with FreeEMS Vanilla. Not all devices will support all functions, either because they have limited functionality (a display device for example), or because the software versions may differ. Where logging/debug facilities are available, the payload type of unrecognised packets should be noted before discarding them.
Payload Type Definitions

Title: updateBlockInRAM
Description: Replaces a block of RAM memory with the provided data. Some blocks are only allowed to be changed as a whole and not partially, IE, size must match the size of the locationID provided and offset must be zero. General configuration blocks can be adjusted using arbitrary offset and size parameters provided that offset is less than size and size is greater than 0 and less than the locationID size. The locationID provided must have non-zero RAM fields.
Payload ID: 0x0100/256
Length: 7+
Contents: locationID (2), offset (2), size (2), data (1+)

Title: updateBlockInFlash
Description: Exactly the same as updateBlockInRAM except for flash memory, and updates the corresponding RAM region if there is one. The locationID provided must have non-zero flash fields.
Payload ID: 0x0102/258
Length: 7+
Contents: locationID (2), offset (2), size (2), data (1+)

Title: retrieveBlockFromRAM
Description: Exactly as per the title. The locationID provided must have non-zero RAM fields. Size of zero returns entire block.
Payload ID: 0x0104/260
Length: 6
Contents: locationID (2), offset (2), size (2)
Reply: requestedData (1+)

Title: retrieveBlockFromFlash
Description: Exactly as per the title. The locationID provided must have non-zero flash fields. Size of zero returns entire block.
Payload ID: 0x0106/262
Length: 6
Contents: locationID (2), offset (2), size (2)
Reply: requestedData (1+)

Title: burnBlockFromRamToFlash
Description: Burn data from live tuned RAM down to persistent flash storage. The locationID provided must have non-zero values for all RAM and flash fields.
Length: 6
Payload ID: 0x0108/264
Contents: locationID (2), offset (2), size (2)

Title: requestBasicDatalog
Description: Request a basic datalog packet to be sent back, useful when not streaming. The optional payload contents are the truncation length to be used. If it is not provided the configured truncation length will be used just as in asynchronous mode.
Payload ID: 0x0190/400
Length: 0 or 2
Contents: Optional Length (2)
Reply: requestedData (1+)

Title: requestConfigurableDatalog
Description: UNIMPLEMENTED
Payload ID: 0x0192/402
Length: ?
Contents: ?
Reply: requestedData (1+)

Title: setAsyncDatalogType
Status: DEPRECATED – use RAM sub-region manipulation to change this. Invalid types will not stream anything. Will be removed in future, new applications should not use this.
Description: Configure the asynchronous datalog type 0x00/0 is off, other values turn specific types of logging on.
Payload ID: 0x0194/404
Length: 1
Contents: datalogType (1)

Title: forwardPacketOverCAN
Description: UNIMPLEMENTED
Payload ID: 0x01F4/500
Length: ?
Contents: ?

Title: forwardPacketOverOtherUART
Description: UNIMPLEMENTED
Payload ID: 0x01F6/502
Length: ?
Contents: ?

Title: retrieveArbitraryMemory
Description: As per the title, for debugging ONLY, could be removed in future.
Payload ID: 0x0258/600
Length: 6
Contents: length (2), address (2), RAMPage (1), FlashPage (1)
Reply: Original contents (6), requestedData (length)

Title: retrieveListOfLocationIDs
Description: Retrieves a list of 16 bit/2 byte location IDs falling into different categories depending on the single byte listType argument. 0x00 gets ALL locationIDs. 0x01 gets all locationIDs that match at least one mask bit “or”. 0x02 gets all locationIDs that match ALL of the mask bits “and”. See just above the definition of the struct “blockDetails” in the file structs.h for flag bit details.
Payload ID: 0xDA5E/55902
Length: 3
Contents: listType (1), listMask (2)
Reply: 16 bit/2 byte locationIDs (0 – 131072) (always an even number, reality is a much lower count)

Title: retrieveLocationIDDetails
Description: Retrieve the attributes of a location ID. See the definition of the struct “blockDetails” in the file structs.h for flag bit details. Parent is meaningless unless specified in the flags. The pages and addresses are optional.
Payload ID: 0xF8E0/63712
Length: 2
Contents: locationID (2)
Reply: flags (2), parent (2), RAMPage (1), FlashPage (1), RAMAddress (2), FlashAddress (2), size (2)